# Minimum Separation Distances for Construction or Expansion of Confinement Feeding Operation Structures (All Animal Feeding Operations, including SAFO)

Instructions:

- Determine if you own or manage another confinement operation that is located within 2,500 feet; or that utilize a common system for manure storage regardless of how far they are apart. If the answer is "yes", you must first contact the Animal Feeding Operations Program at (712) 262-4177 or your nearest DNR Field Office, before proceeding with separation distance determination.

- Complete Worksheet No. 1 (page 2) to determine the Animal Unit Capacity (AUC).

- Complete Worksheet No. 2 (page 2), to determine the Animal Weight Capacity (AWC), however, this only applies to an operation that was constructed prior to March 1, 2003.

- Determine the year when the operation was constructed. This is the date when any of the following occurred:

  - Excavation of a structure or excavation of the footings of a structure.

  - Installation of forms for concrete of a structure.

  - Installation of piping to transport manure between confinement feeding operation structures.

- Select the Table that applies, based on the year when the operation was constructed and the animal species, according to the following:

| a) Table 6: New operation or expansion of an operation that was or will be constructed on or after March 1, 2003, for all animal species. | Page 3 |
| --- | --- |
| b) Table 6-A: Expansion or modification of an operation that was constructed on or after January 1, 1999 but prior to March 1, 2003, for animals other than bovine (swine, sheep, horses, poultry). | Page 4 |
| c) Table 6-B: Expansion or modification of an operation that was constructed on or after January 1, 1999 but prior to March 1, 2003, for bovine (beef, dairy). | Page 5 |
| d) Table 6-C: Expansion or modification of an operation that was constructed prior to January 1, 1999, for animals other than bovine (swine, sheep, horses, poultry). | Page 6 |
| e) Table 6-D: Expansion or modification of an operation that was constructed prior to January 1, 1999, for bovine (beef, dairy). | Page 7 |

- Distances to a residence, business, church, school or public use area: In the appropriate table, select the type of structure being constructed, expanded or modified. Use the AUC or AWC [whichever applies], to select the appropriate range for AUC or AWC, and the minimum required separation distances.

- Distances to water wells: In the middle portion of the appropriate table, select the type of structure being constructed, expanded or modified. To determine if a well is deep or shallow, use the well log record. A 'deep well' is defined in 567 IAC 65.1(455B). Distances to wells are required to all animal feeding operations (SAFO1s included).

- Distance to major water sources, sinkholes, water sources, designated wetlands, environmentally sensitive areas and public thoroughfares: In the bottom part of the appropriate table, find these distance requirements that apply to all animal feeding operations (SAFO1s included, unless specifically exempted). Major water sources are listed in 567 IAC 65, Tables 1 and 2.

| For more information, contact one of these DNR offices or visit: www.iowadnr.gov AFO Construction Permits 1900 N Grand Ave Spencer IA 51301 (712) 262-4177 | Field Office 1 1101 Commercial Ct Ste 10 Manchester IA 52057 (563) 927-2640 | Field Office 3 1900 N Grand Ave Spencer IA 51301 (712) 262-4177 | Field Office 5 502 E 9th St Des Moines IA 50319 (515) 725-0268 |
| --- | --- | --- | --- |
|  | Field Office 2 2300 15th St SW Mason City IA 50401 (641) 424-4073 | Field Office 4 1401 Sunnyside Ln Atlantic IA 50022 (712) 243-1934 | Field Office 6 1023 W Madison Washington IA 52353 (319) 653-2135 |

CAUTION: This document is only a summary of Iowa Code chapter 459 (2003) and the DNR’s amended administrative rules. It is a guidance document and should not be used as replacement for the statutory provisions and administrative rules (collectively, the law). While every effort has been made to assure the accuracy of this information, the law will prevail in the event of a conflict between this document and the law.

| Name of Operation: |  | Facility ID No.: |  |
| --- | --- | --- | --- |

## Worksheet 1. Animal Unit Capacity (AUC)

The animal unit capacity (AUC) is the maximum number of animal units (AU) maintained at the operation at any one time. To calculate the AUC, multiply the maximum number of animals confined at any one time by the appropriate AU factor and then add all animal units together. If you own or manage another confinement operation that utilizes a common system for manure storage, or that is located within 2,500 feet, you must first contact the DNR (see page 1):

| Animal Species | Current | Proposed Expansion (No. of animals to be added) | Total |
| --- | --- | --- | --- |
|  | (No. Head) | x (Factor) | = AUC | (No. Head) | x (Factor) | = AUC | (No. Head) | x (Factor) | = AUC |
| Slaughter or feeder cattle |  | 1.0 |  |  | 1.0 |  |  | 1.0 |  |
| Immature dairy cattle |  | 1.0 |  |  | 1.0 |  |  | 1.0 |  |
| Mature dairy cattle |  | 1.4 |  |  | 1.4 |  |  | 1.4 |  |
| Gestating sows |  | 0.4 |  |  | 0.4 |  |  | 0.4 |  |
| Farrowing sows & litter |  | 0.4 |  |  | 0.4 |  |  | 0.4 |  |
| Boars |  | 0.4 |  |  | 0.4 |  |  | 0.4 |  |
| Gilts |  | 0.4 |  |  | 0.4 |  |  | 0.4 |  |
| Finished (Market) hogs |  | 0.4 |  |  | 0.4 |  |  | 0.4 |  |
| Nursery pigs 15 lbs to 55 lbs |  | 0.1 |  |  | 0.1 |  |  | 0.1 |  |
| Sheep and lambs |  | 0.1 |  |  | 0.1 |  |  | 0.1 |  |
| Horses |  | 2.0 |  |  | 2.0 |  |  | 2.0 |  |
| Turkeys 7lbs or more |  | 0.018 |  |  | 0.018 |  |  | 0.018 |  |
| Turkeys less than 7 lbs |  | 0.0085 |  |  | 0.0085 |  |  | 0.0085 |  |
| Broiler/Layer chickens 3 lbs or more |  | 0.01 |  |  | 0.01 |  |  | 0.01 |  |
| Broiler/Layer chickens less than 3 lbs |  | 0.0025 |  |  | 0.0025 |  |  | 0.0025 |  |
| Fish |  | 0.001 |  |  | 0.001 |  |  | 0.001 |  |
| TOTALS: | Current: |  | Proposed Expansion: |  | Total: |  |

## Worksheet 2. Animal Weight Capacity (AWC)

Only applies to operations that were first constructed prior to March 1, 2003. The animal weight capacity (AWC) is the product of multiplying the maximum number of animals confined at any one time by their average weight during the production cycle. Use the AWC definition and its examples set forth in rule 567 IAC 65.1(455B). Then add the AWC if more than one animal species is present.

| Animal Species | Existing AWC (Before Permit) | Proposed Expansion (No. of animals to be added) | Total |
| --- | --- | --- | --- |
|  | (No. head) x | avg weight | = AWC | (No. head) x | avg weight | = AWC | (No. head) x | avg weight | = AWC |
| Slaughter or feeder cattle |  |  |  |  |  |  |  |  |  |
| Immature dairy cattle |  |  |  |  |  |  |  |  |  |
| Mature dairy cattle |  |  |  |  |  |  |  |  |  |
| Gestating sows |  |  |  |  |  |  |  |  |  |
| Farrowing sows & litter |  |  |  |  |  |  |  |  |  |
| Boars |  |  |  |  |  |  |  |  |  |
| Gilts |  |  |  |  |  |  |  |  |  |
| Finished (Market) hogs |  |  |  |  |  |  |  |  |  |
| Nursery pigs 15 lbs to 55 lbs |  |  |  |  |  |  |  |  |  |
| Sheep and lambs |  |  |  |  |  |  |  |  |  |
| Horses |  |  |  |  |  |  |  |  |  |
| Turkeys 7lbs or more |  |  |  |  |  |  |  |  |  |
| Turkeys less than 7 lbs |  |  |  |  |  |  |  |  |  |
| Broiler/Layer chickens 3 lbs or more |  |  |  |  |  |  |  |  |  |
| Broiler/Layer chickens less than 3 lbs |  |  |  |  |  |  |  |  |  |
| Fish |  |  |  |  |  |  |  |  |  |
| TOTALS: | Current: |  | Proposed Expansion: |  | Total: |  |

## Table 6 567 IAC 65.11(455B)

Minimum separation distances for a new confinement feeding operation or expansion of an operation constructed on or after March 1, 2003

| Type of Structure (liquid, semi-liquid and dry manure storage) | Total Animal Unit Capacity (AUC) (AU) | Residences, Businesses, Churches, Schools | Public use areas |
| --- | --- | --- | --- |
|  |  | Unincorporated Areas | Incorporated Areas |  |
| Anaerobic lagoons and uncovered earthen manure storage basins | 500 AU or less | 1,875 feet | 1,875 feet | 1,875 feet |
|  | 501 AU to <1,000 AU | 1,875 feet | 1,875 feet | 1,875 feet |
|  | 1,000 AU to <3,000 AU | 2,500 feet | 2,500 feet | 2,500 feet |
|  | 3,000 AU or more | 3,000 feet | 3,000 feet | 3,000 feet |
| Covered earthen manure storage basins | 500 AU or less | 1,250 feet | 1,875 feet | 1,875 feet |
|  | 501 AU to <1,000 AU | 1,250 feet | 1,875 feet | 1,875 feet |
|  | 1,000 AU to <3,000 AU | 1,875 feet | 2,500 feet | 2,500 feet |
|  | 3,000 AU or more | 2,375 feet | 3,000 feet | 3,000 feet |
| Uncovered formed manure storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <1,000 AU | 1,500 feet | 1,875 feet | 1,875 feet |
|  | 1,000 AU to <3,000 AU | 2,000 feet | 2,500 feet | 2,500 feet |
|  | 3,000 AU or more | 2,500 feet | 3,000 feet | 3,000 feet |
| Confinement buildings and covered formed manure storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <1,000 AU | 1,250 feet | 1,875 feet | 1,875 feet |
|  | 1,000 AU to <3,000 AU | 1,875 feet | 2,500 feet | 2,500 feet |
|  | 3,000 AU or more | 2,375 feet | 3,000 feet | 3,000 feet |
| Egg washwater storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <1,000 AU | 1,000 feet | 1,875 feet | 1,875 feet |
|  | 1,000 AU to <3,000 AU | 1,500 feet | 2,500 feet | 2,500 feet |
|  | 3,000 AU or more | 2,000 feet | 3,000 feet | 3,000 feet |

Distances to Wells - Applies to all Confinement Feeding Operations, regardless of animal unit capacity.

| Type of Structure | Public well | Private well |
| --- | --- | --- |
|  | Shallow | Deep | Shallow | Deep |
| Aerobic structure, anaerobic lagoon, earthen manure storage basin, egg washwater storage structure. | 1,000 feet | 400 feet | 400 feet | 400 feet |
| Formed manure storage structure, confinement building | 200 feet | 100 feet | 200 feet | 100 feet |

Other Distances - Applies to all Confinement Feeding Operations, regardless of animal unit capacity

| Surface intakes of an agricultural drainage well or water source other than major (Excluding farm ponds, privately owned lakes or when a secondary containment barrier is provided) | 500 feet* |
| --- | --- |
| Wellhead or cistern of an agricultural drainage well or known sinkhole or major water source (Excluding farm ponds, privately owned lakes or when a secondary containment barrier is provided) | 1,000 feet |
| Designated wetlands pursuant to subrule 65.11(4) and Iowa Code section 459.310 | 2,500 feet |
| Right-of-way of a thoroughfare maintained by the state or a political subdivision (Exemptions provided in subrule 65.12(2)) | 100 feet |

*200 feet from a water source required for a dry bedded confinement feeding operation structure.

## TABLE 6-A (Swine, Sheep, Horses and Poultry)

Minimum separation distances for expansion of confinement feeding operations constructed on or after January 1, 1999 but prior to March 1, 2003

| Type of Structure (liquid, semi-liquid and dry manure storage) | Size of operation AUC (AU) and AWC (lbs) | Residences, Businesses, Churches, Schools | Public use areas |
| --- | --- | --- | --- |
|  |  | Unincorporated Areas | Incorporated Areas |  |
| Anaerobic lagoons and uncovered earthen manure storage basins | 500 AU or less | 1,250 feet | 1,250 feet | 1,250 feet |
|  | 501 AU to <625,000 lbs | 1,250 feet | 1,250 feet | 1,250 feet |
|  | 625,000 lbs to <1,250,000 lbs | 1,875 feet | 1,875 feet | 1,875 feet |
|  | 1,250,000 lbs or more | 2,500 feet | 2,500 feet | 2,500 feet |
| Covered earthen manure storage basins | 500 AU or less | 1,000 feet | 1,250 feet | 1,250 feet |
|  | 501 AU to <625,000 lbs | 1,000 feet | 1,250 feet | 1,250 feet |
|  | 625,000 lbs to <1,250,000 lbs | 1,250 feet | 1,875 feet | 1,875 feet |
|  | 1,250,000 lbs or more | 1,875 feet | 2,500 feet | 2,500 feet |
| Uncovered formed manure storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <625,000 lbs | 1,250 feet | 1,250 feet | 1,250 feet |
|  | 625,000 lbs to <1,250,000 lbs | 1,500 feet | 1,875 feet | 1,875 feet |
|  | 1,250,000 lbs or more | 2,000 feet | 2,500 feet | 2,500 feet |
| Confinement buildings and covered formed manure storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <625,000 lbs | 1,000 feet | 1,250 feet | 1,250 feet |
|  | 625,000 lbs to <1,250,000 lbs | 1,250 feet | 1,875 feet | 1,875 feet |
|  | 1,250,000 lbs or more | 1,875 feet | 2,500 feet | 2,500 feet |
| Egg washwater storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <625,000 lbs | 750 feet | 1,250 feet | 1,250 feet |
|  | 625,000 lbs to <1,250,000 lbs | 1,000 feet | 1,875 feet | 1,875 feet |
|  | 1,250,000 lbs or more | 1,500 feet | 2,500 feet | 2,500 feet |

Distances to Wells - Applies to all Confinement Feeding Operations, regardless of animal unit capacity.

| Type of Structure | Public well | Private well |
| --- | --- | --- |
|  | Shallow | Deep | Shallow | Deep |
| Aerobic structure, anaerobic lagoon, earthen manure storage basin, egg washwater storage structure. | 1,000 feet | 400 feet | 400 feet | 400 feet |
| Formed manure storage structure, confinement building | 200 feet | 100 feet | 200 feet | 100 feet |

Other Distances - Applies to all Confinement Feeding Operations, regardless of animal unit capacity

| Surface intakes of an agricultural drainage well or water source other than major (Excluding farm ponds, privately owned lakes or when a secondary containment barrier is provided) | 500 feet* |
| --- | --- |
| Wellhead or cistern of an agricultural drainage well or known sinkhole or major water source (Excluding farm ponds, privately owned lakes or when a secondary containment barrier is provided) | 1,000 feet |
| Designated wetlands pursuant to subrule 65.11(4) and Iowa Code section 459.310 | 2,500 feet |
| Right-of-way of a thoroughfare maintained by the state or a political subdivision (Exemptions provided in subrule 65.12(2)) | 100 feet |

*200 feet from a water source required for a dry bedded confinement feeding operation structure.

## TABLE 6-B (Beef and Dairy Cattle)

Minimum separation distances for expansion of a confinement feeding operation constructed on or after January 1, 1999 but prior to March 1, 2003

| Type of Structure (liquid, semi-liquid and dry manure storage) | Size of operation AUC (AU) and AWC (lbs) | Residences, Businesses, Churches, Schools | Public use areas |
| --- | --- | --- | --- |
|  |  | Unincorporated Areas | Incorporated Areas |  |
| Anaerobic lagoons and uncovered earthen manure storage basins | 500 AU or less | 1,250 feet | 1,250 feet | 1,250 feet |
|  | 501 AU to <1,600,000 lbs | 1,250 feet | 1,250 feet | 1,250 feet |
|  | 1,600,000 lbs to <4,000,000 lbs | 1,875 feet | 1,875 feet | 1,875 feet |
|  | 4,000,000 lbs or more | 2,500 feet | 2,500 feet | 2,500 feet |
| Covered earthen manure storage basins | 500 AU or less | 1,000 feet | 1,250 feet | 1,250 feet |
|  | 501 AU to <1,600,000 lbs | 1,000 feet | 1,250 feet | 1,250 feet |
|  | 1,600,000 lbs to <4,000,000 lbs | 1,250 feet | 1,875 feet | 1,875 feet |
|  | 4,000,000 lbs or more | 1,875 feet | 2,500 feet | 2,500 feet |
| Uncovered formed manure storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <1,600,000 lbs | 1,250 feet | 1,250 feet | 1,250 feet |
|  | 1,600,000 lbs to <4,000,000 lbs | 1,500 feet | 1,875 feet | 1,875 feet |
|  | 4,000,000 lbs or more | 2,000 feet | 2,500 feet | 2,500 feet |
| Confinement buildings and covered formed manure storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <1,600,000 lbs | 1,000 feet | 1,250 feet | 1,250 feet |
|  | 1,600,000 lbs to <4,000,000 lbs | 1,250 feet | 1,875 feet | 1,875 feet |
|  | 4,000,000 lbs or more | 1,875 feet | 2,500 feet | 2,500 feet |

Distances to Wells - Applies to all Confinement Feeding Operations, regardless of animal unit capacity.

| Type of Structure | Public well | Private well |
| --- | --- | --- |
|  | Shallow | Deep | Shallow | Deep |
| Aerobic structure, anaerobic lagoon, earthen manure storage basin, egg washwater storage structure. | 1,000 feet | 400 feet | 400 feet | 400 feet |
| Formed manure storage structure, confinement building | 200 feet | 100 feet | 200 feet | 100 feet |

Other Distances - Applies to all Confinement Feeding Operations, regardless of animal unit capacity

| Surface intakes of an agricultural drainage well or water source other than major (Excluding farm ponds, privately owned lakes or when a secondary containment barrier is provided) | 500 feet* |
| --- | --- |
| Wellhead or cistern of an agricultural drainage well or known sinkhole or major water source (Excluding farm ponds, privately owned lakes or when a secondary containment barrier is provided) | 1,000 feet |
| Designated wetlands pursuant to subrule 65.11(4) and Iowa Code section 459.310 | 2,500 feet |
| Right-of-way of a thoroughfare maintained by the state or a political subdivision (Exemptions provided in subrule 65.12(2)) | 100 feet |

*200 feet from a water source required for a dry bedded confinement feeding operation structure.

## TABLE 6-C (Swine, Sheep, Horses and Poultry)

Minimum separation distances for expansion of a confinement feeding operation constructed prior to January 1, 1999

| Type of Structure (liquid, semi-liquid and dry manure storage) | Size of operation AUC (AU) and AWC (lbs) | Residences, Businesses, Churches, Schools | Public use areas |
| --- | --- | --- | --- |
|  |  | Unincorporated Areas | Incorporated Areas |  |
| Anaerobic lagoons and uncovered earthen manure storage basins | 500 AU or less | 1,250 feet | 1,250 feet | 1,250 feet |
|  | 501 AU to <625,000 lbs | 1,250 feet | 1,250 feet | 1,250 feet |
|  | 625,000 lbs to <1,250,000 lbs | 1,875 feet | 1,875 feet | 1,875 feet |
|  | 1,250,000 lbs or more | 2,500 feet | 2,500 feet | 2,500 feet |
| Covered earthen manure storage basins | 500 AU or less | 750 feet | 1,250 feet | 1,250 feet |
|  | 501 AU to <625,000 lbs | 750 feet | 1,250 feet | 1,250 feet |
|  | 625,000 lbs to <1,250,000 lbs | 1,000 feet | 1,875 feet | 1,875 feet |
|  | 1,250,000 lbs or more | 1,500 feet | 2,500 feet | 2,500 feet |
| Uncovered formed manure storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <625,000 lbs | 1,000 feet | 1,250 feet | 1,250 feet |
|  | 625,000 lbs to <1,250,000 lbs | 1,500 feet | 1,875 feet | 1,875 feet |
|  | 1,250,000 lbs or more | 2,000 feet | 2,500 feet | 2,500 feet |
| Confinement buildings and covered formed manure storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <625,000 lbs | 750 feet | 1,250 feet | 1,250 feet |
|  | 625,000 lbs to <1,250,000 lbs | 1,000 feet | 1,875 feet | 1,875 feet |
|  | 1,250,000 lbs or more | 1,500 feet | 2,500 feet | 2,500 feet |
| Egg washwater storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <625,000 lbs | 750 feet | 1,250 feet | 1,250 feet |
|  | 625,000 lbs to <1,250,000 lbs | 1,000 feet | 1,875 feet | 1,875 feet |
|  | 1,250,000 lbs or more | 1,500 feet | 2,500 feet | 2,500 feet |

Distances to Wells - Applies to all Confinement Feeding Operations, regardless of animal unit capacity.

| Type of Structure | Public well | Private well |
| --- | --- | --- |
|  | Shallow | Deep | Shallow | Deep |
| Aerobic structure, anaerobic lagoon, earthen manure storage basin, egg washwater storage structure. | 1,000 feet | 400 feet | 400 feet | 400 feet |
| Formed manure storage structure, confinement building | 200 feet | 100 feet | 200 feet | 100 feet |

Other Distances - Applies to all Confinement Feeding Operations, regardless of animal unit capacity

| Surface intakes of an agricultural drainage well or water source other than major (Excluding farm ponds, privately owned lakes or when a secondary containment barrier is provided) | 500 feet* |
| --- | --- |
| Wellhead or cistern of an agricultural drainage well or known sinkhole or major water source (Excluding farm ponds, privately owned lakes or when a secondary containment barrier is provided) | 1,000 feet |
| Designated wetlands pursuant to subrule 65.11(4) and Iowa Code section 459.310 | 2,500 feet |
| Right-of-way of a thoroughfare maintained by the state or a political subdivision (Exemptions provided in subrule 65.12(2)) | 100 feet |

*200 feet from a water source required for a dry bedded confinement feeding operation structure.

## TABLE 6-D (Beef and Dairy Cattle)

Minimum separation distances for expansion of a confinement feeding operations constructed prior to January 1, 1999

| Type of Structure (liquid, semi-liquid and dry manure storage) | Size of operation AUC (AU) and AWC (lbs) | Residences, Businesses, Churches, Schools | Public use areas |
| --- | --- | --- | --- |
|  |  | Unincorporated Areas | Incorporated Areas |  |
| Anaerobic lagoons and uncovered earthen manure storage basins | 500 AU or less | 1,250 feet | 1,250 feet | 1,250 feet |
|  | 501 AU to <1,600,000 lbs | 1,250 feet | 1,250 feet | 1,250 feet |
|  | 1,600,000 lbs to <4,000,000 lbs | 1,875 feet | 1,875 feet | 1,875 feet |
|  | 4,000,000 lbs or more | 2,500 feet | 2,500 feet | 2,500 feet |
| Covered earthen manure storage basins | 500 AU or less | 750 feet | 1,250 feet | 1,250 feet |
|  | 501 AU to <1,600,000 lbs | 750 feet | 1,250 feet | 1,250 feet |
|  | 1,600,000 lbs to <4,000,000 lbs | 1,000 feet | 1,875 feet | 1,875 feet |
|  | 4,000,000 lbs or more | 1,500 feet | 2,500 feet | 2,500 feet |
| Uncovered formed manure storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <1,600,000 lbs | 1,000 feet | 1,250 feet | 1,250 feet |
|  | 1,600,000 lbs to <4,000,000 lbs | 1,500 feet | 1,875 feet | 1,875 feet |
|  | 4,000,000 lbs or more | 2,000 feet | 2,500 feet | 2,500 feet |
| Confinement buildings and covered formed manure storage structures | 500 AU or less | None | None | None |
|  | 501 AU to <1,600,000 lbs | 750 feet | 1,250 feet | 1,250 feet |
|  | 1,600,000 lbs to <4,000,000 lbs | 1,000 feet | 1,875 feet | 1,875 feet |
|  | 4,000,000 lbs or more | 1,500 feet | 2,500 feet | 2,500 feet |

Distances to Wells - Applies to all Confinement Feeding Operations, regardless of animal unit capacity.

| Type of Structure | Public well | Private well |
| --- | --- | --- |
|  | Shallow | Deep | Shallow | Deep |
| Aerobic structure, anaerobic lagoon, earthen manure storage basin, egg washwater storage structure. | 1,000 feet | 400 feet | 400 feet | 400 feet |
| Formed manure storage structure, confinement building | 200 feet | 100 feet | 200 feet | 100 feet |

Other Distances - Applies to all Confinement Feeding Operations, regardless of animal unit capacity

| Surface intakes of an agricultural drainage well or water source other than major (Excluding farm ponds, privately owned lakes or when a secondary containment barrier is provided) | 500 feet* |
| --- | --- |
| Wellhead or cistern of an agricultural drainage well or known sinkhole or major water source (Excluding farm ponds, privately owned lakes or when a secondary containment barrier is provided) | 1,000 feet |
| Designated wetlands pursuant to subrule 65.11(4) and Iowa Code section 459.310 | 2,500 feet |
| Right-of-way of a thoroughfare maintained by the state or a political subdivision (Exemptions provided in subrule 65.12(2)) | 100 feet |

*200 feet from a water source required for a dry bedded confinement feeding operation structure.

# Footnotes

SAFO= A small animal feeding operation, which has an animal unit capacity of 500 animal units (AU) or less.